## Slide 1: CPE 390: Microprocessor Systems Spring 2018
Lecture 14
Analog to Digital Conversion
Bryan Ackland
Department of Electrical and Computer Engineering
Stevens Institute of Technology
Hoboken, NJ 07030
Adapted from HCS12/9S12 An Introduction to Software and Hardware Interfacing Han-Way Huang, 2010

## Slide 2: The Real World of Analog
A microprocessor deals exclusively with digital data
  finite precision representations of external real world and internal computational data
A microcontroller in an embedded application takes inputs from real-world sensors
  some of these are already digital (e.g. switches, keyboard, mouse)
  many are analog (e.g. pressure, temperature, light intensity, microphone, airflow, engine speed, oxygen level)
Analog-to-Digital converter (A/D) transforms analog signal into digital representation usable by microprocessor
Transducer
(sensor)
Signal
Conditioning
A/D
Converter
Micro-
processor
digital
value
voltage
voltage
temp
sound
light
thermometer
microphone
photodiode
both in time
and value
quantized
in time
and value

## Slide 3: Analog to Digital Conversion
An A/D converter samples an analog signal at regular intervals and generates a digital code which is its best (closest) approximation to the analog value at that instant
Analog signal: continuous in time and value
Digital signal: quantized in time and value
analog
input
voltage
digital
code
levels
1.0V
2.0V
0000
1000
1111
0
1
2
3
4
5
6
sampling intervals
1101
1110
1101
1001
0101
0101
1001

## Slide 4: A/D Transfer Function
An n-bit A/D converter has possible output codes
Input voltage range typically defined by two reference voltages VRL and VRH
input
voltage
output
code
quantization
error (Qerr )

## Slide 5: A/D Characteristics
Resolution
  often quoted in terms of # bits (e.g. 12-bit converter)
  analog resolution is
  average conversion error =
Conversion time
  how long does it take to produce digital code
Maximum Sampling Frequency
  How many samples per second
  Limits maximum frequency component of analog input that is accurately captured by the A/D (see Nyquist)
Linearity
  staircase has uneven steps
  generates error in addition to quantization error
  significant non-linearity can lead to non-monoticity (e.g. a higher voltage generates a smaller code)

## Slide 6: Flash (Parallel) A/D Converter
Resistor ladder generates 2n reference voltages
2n comparators simultaneously compare input with each reference
Comparator output k is high if Vin > refk
Conversion logic generates code indicating greatest value of k for which comparator output is high
Very high speed
Expensive in area & power
Limited to ~ 8-bits
R/2
R/2
+
–
+
–
+
–
+
–
thermo-meter
to binary
convert
R
R
R
VRH
VRL
Vin
n-bit
digital
output

## Slide 7: Single Slope A/D Converter
Compares input to linear ramp to generate a pulse width proportional to Vin
Pulse used to gate clock to high speed digital counter
Simple hardware – popular in low speed applications
High resolution possible
Performance limited by:
Ramp
Generator
+
–
n-bit
counter
Vin
reset
high
speed
clock
n-bit
digital output
e.g. for = 1 MHz, a 12-bit converter requires = 4 GHz

## Slide 8: Counter Ramp A/D Converter
Variant on single-slope converter
Ramp is generated by counter driving a D/A converter
When D/A output ramp crosses Vin, counter value is captured in n-bit latch
Does not require precision analog ramp generation
Precision limited by linearity of D/A
Vin
n-bit D/A
+
–
n-bit
counter
reset
n-bit
digital output
n-bit
latch

## Slide 9: Sigma Delta (Oversampling) A/D Converter
Sigma-delta modulator consists of summer, integrator, clocked comparator and a 1-bit DAC
Modulator runs at many times (e.g. 16x – 1000x) the required sampling frequency to produce very high speed 1-bit waveform
Digital filter coverts this to much slower n-bit digital output
Since 1-bit DAC is perfectly linear, can produce very high resolution (up to 24-bit)
Sampling frequency is limited by need to over-sample
1-bit
DAC
+
S
–
Vin
Digital
Filter
(Decimator)
n-bit
digital
output
Sigma-Delta Modulator

## Slide 10: Successive Approximation A/D Converter
Guesses and then corrects digital code in SAR one bit at a time
Initially sets all bits in SAR to ‘0’
Then starting with MSB, for each bit:
  set bit to ‘1’ and convert output of SAR to analog value with D/A
  compare output of D/A to input voltage
  if D/A is larger, set this bit back to ‘0’ and go on to next (lesser sig.) bit
  if input is larger, retain ‘1’ for this bit and go on to next bit
Successive Approximation Register
n-bit D/A Converter
Dn-1
Dn-2
D0
D1
D2
+
–
Control Logic
Vin
n-bit
digital
output
VRH
VRL

## Slide 11: Successive Approximation Process
SAR gives a good tradeoff between speed and precision
One of most popular A/D techniques in embedded systems
Used in HCS12
000
1XX
11X
01X
111
101
011
001
111
110
101
100
011
010
001
analog
input
digital
output
(010)

## Slide 12: Signal Conditioning
Signal Conditioning is process of matching transducer output to input characteristics of A/D
  Need to match in voltage and time (frequency)
Input range of A/D defined by VRH and VRL
  Unlikely to match output range of transducer
  e.g. transducer may output signal (-1 to +1 V), whereas A/D has input range of (0 to 4V).
  Need “scale & shift circuit” to scale by x2 and shift by +2V.
If sampling rate of A/D if samples/sec, maximum frequency correctly captured is
  Any components of higher frequency content will be aliased
  Signal conditioning may need low pass filter
Transducer
(sensor)
Signal
Conditioning
A/D
Converter
Micro-
processor
digital
value
voltage
voltage
temp
sound
light

## Slide 13: Shift & Scale Circuit
From previous example, if R1 = R3 = 10kW, R2 = 20kW, VOFF = -1V:
+
–
741
+ 12V
– 12V
VOFF
VIN
+
–
741
+ 12V
– 12V
R2
R1
R0
R0
VOUT
R3

## Slide 14: Nyquist Frequency
If is the sampling frequency,
Any signal component above Nyquist frequency will be aliased back into sampled waveform as a lower frequency component

## Slide 15: Aliasing
Even if desired signal does not contain components > Nyquist, there may be high frequency noise components which must be removed
Signal conditioning circuits frequently include a sharp low-pass filter to take out any signal components > Nyquist

## Slide 16: A/D Conversion on HCS12
HCS12 may have one or two 8-channel 10-bit A/D’s
Each uses successive approximation method
A/D’s runs off an ATD clock that can be set 500kHz ~ 2 MHz
  At 2 MHz, ADC can perform an 8-bit conversion in 6ms or a 10-bit conversion in 7 ms.
A/D conversion may be internally triggered (by writing to a control register) or externally triggered (via pins AN7 or AN15)
May be a single conversion or a sequence of conversions
Result(s) can be 8-bit or 10-bit, signed or unsigned:
  (–128 to +127) or (–512 to +511) signed
  (0 to 255) or (0 to 1023) unsigned
Result(s) stored in 16-bit register(s)
  either left or right justified

## Slide 17: ATD Block Diagram

## Slide 18: A/D Pins & Registers
Signal Pins:
  AD0 module uses pins AN0 ~ AN7
  AD1 module uses pins AN8 ~ AN15
  AN7 (AN15) pin can optionally be used to trigger AD0 (AD1) module
  VRH and VRL are high and low reference voltage inputs
  VDDA and VSSA are power supply and ground pins
Each A/D has following registers:
  Six control registers ATDxCTL0 ~ ATDxCTL5
    (0 and 1 for factory testing only)
  Two status registers ATDxSTAT0 ~ ATDxSTAT1
  One input enable register ADTxDIEN
  One port data register PTADx
  Eight 16-bit result registers ATDxDR0 ~ ATDxDR7
  where x= 0 or 1 (we will only describe AD0 registers in following slides)

## Slide 19: ATD Control Register 2 (ATD0CTL2)
ADPU: ATD power-down bit (‘0’: power-down, ‘1’: normal ATD operation)
AFFC: ATD fast flag clear bit
‘0’: ATD flag is cleared normally (i.e. read status before reading result)
‘1’: Any access to ATD result register will cause associated CCF flag to clear
AWAI: Power-down in wait mode (‘0’: ATD runs in wait, ‘1’: does not run in wait)*
ETRIGLE: External trigger level/edge control (see next slide)
ETRIGP: External trigger polarity (see next slide)
ETRIGE: External trigger mode enable (‘0’: disable trigger on ATD channel 7, ‘1’: enable trigger on ATD channel 7)
ASCIE: ATD sequence complete interrupt enable bit (‘0’: disabled, ‘1’: enabled)
ASCIF: ATD sequence complete interrupt flag
ADPU
AFFC
AWAI
ETRIGLE
ETRIGP
ETRIGE
ASCIE
ASCIF
7
6
5
4
3
2
1
0
0
0
0
0
0
0
0
0
Reset:
* We will not be using these bits

## Slide 20: Notes on ATD0CTL2
ASCIF flag signals that a requested multi-sample sequence conversion sequence has completed (see ATD0CTL3)
  If ASCIE is set, this will also cause interrupt
Writing to ATD0CTL2 will abort any current conversion sequence
ETRIGLE | ETRIGP | External Trigger Sensitivity
0 | 0 | Falling edge
0 | 1 | Rising Edge
1 | 0 | Low level
1 | 1 | High level

## Slide 21: ATD Control Register 3 (ATD0CTL3)
S8C, S4C, S2C, S1C: Conversion Sequence Length
0000 = 8 conversions
0001 = 1 conversions
0010 = 2 conversions
0011 = 3 conversions
0100 = 4conversions
FIFO: Result register FIFO mode (always set this bit to ‘0’)*
FRZ1, FRZ0: Background debug freeze enable bit (ignore these bits)*
Writing to ATD0CTL3 will abort any current conversion sequence
0
S8C
S4C
S2C
S1C
FIFO
FRZ1
FRZ0
7
6
5
4
3
2
1
0
0
0
1
0
0
0
0
0
Reset:
0101 = 5 conversions
0110 = 6 conversions
0111 = 7 conversions
1xxx = 8 conversions

## Slide 22: ATD Control Register 4 (ATD0CTL4)
SRES8: ATD resolution select bit (‘0’: 10-bit operation, ‘1’: 8-bit operation)
SMP1, SMP0: Select Sample Time bits (see next slide)
PRS4 ~ PRS0: ATD clock pre-scaler bits.
(ATD clock must be between 500kHz and 2 MHz)
Writing to ATD0CTL4 will abort any current conversion sequence
SRES8
SMP1
SMP0
PRS4
PRS3
PRS2
PRS1
PRS0
7
6
5
4
3
2
1
0
0
0
0
0
0
1
0
1
Reset:

## Slide 23: Sample Time Select
Sampling process has two stages:
  Initially a unity gain sampling amplifier buffers input signal for two cycles to rapidly charge sample capacitor to almost the input potential
  Sample buffer is then disconnected and input is connected directly to sample capacitor for 2, 4, 8 or 16 cycles
+1
Sample & Hold
+1
Analog
Input
To
Comparator
SMP1 | SMP0 | Length of 2nd Phase of Sample Time
0 | 0 | 2 ATD clock periods
0 | 1 | 4 ATD clock periods
1 | 0 | 8 ATD clock periods
1 | 1 | 16 ATD clock periods

## Slide 24: ATD Control Register 5 (ATD0CTL5)
DJM: Result register data justification (‘0’: left justified, ‘1’: right justified)#
DSGN: Result register signed representation (‘0’: unsigned, ‘1’: signed)#
SCAN: Continuous channel scan bit (always set this bit to ‘0’)*
MULT: Enable multichannel conversion bit
‘0’: Sample only one channel (specified by CC/CB/CA)
‘1’: Sample across several channels (start with CC/CB/CA; number of channels specified by sequence length)
CC, CB, CA: Channel select code
Three bit code to select input channel (if MULT=0) or first channel in incrementing sequence (if MULT=1)
# cannot be signed and right justified
DJM
DSGN
SCAN
MULT
0
CC
CB
CA
7
6
5
4
3
2
1
0
0
0
0
0
0
0
0
0
Reset:

## Slide 25: Notes on ATD0CTL5
Writing to ATD0CTL5 will abort any current conversion sequence and start a new conversion sequence
SRES8 | DJM | DSGN | Result Data Format | Bit Mapping
1 | 0 | 0 | 8-bit/left-justified/unsigned | bits 15 ~ 8
1 | 0 | 1 | 8-bit/left-justified/signed | bits 15 ~ 8
1 | 1 | x | 8-bit/right-justified/unsigned | bits 7 ~ 0
0 | 0 | 0 | 10-bit/left-justified/unsigned | bits 15 ~ 6
0 | 0 | 1 | 10-bit/left-justified/signed | bits 15 ~ 6
0 | 1 | x | 10-bit/right-justified/unsigned | bits 9 ~ 0

## Slide 26: Input Analog Voltage to Output Code
Left justified codes:
Input signal (V) VRL = 0.000 V VRH = 5.120 V | Signed 8-bit codes (MSByte) | Unsigned 8-bit codes (MSByte) | Signed 10-bit codes | Unsigned 10-bit codes
5.115 | 7F | FF | 7FC0 | FFC0
5.100 | 7F | FF | 7F00 | FF00
2.580 | 01 | 81 | 0100 | 8100
2.565 | 00 | 80 | 0040 | 8040
2.560 | 00 | 80 | 0000 | 8000
2.555 | 00 | 80 | FFC0 | 7FC0
2.540 | FF | 7F | FF00 | 7F00
0.020 | 81 | 01 | 8100 | 0100
0.005 | 80 | 00 | 8040 | 0040
0.000 | 80 | 00 | 8000 | 0000

## Slide 27: Input Analog Voltage to Output Code
Right justified codes:
Input signal (V) VRL = 0.000 V VRH = 5.120 V | Signed 8-bit codes (LSByte) | Unsigned 8-bit codes (LSByte) | Signed 10-bit codes | Unsigned 10-bit codes
5.115 |  | FF |  | 03FF
5.100 |  | FF |  | 03FC
2.580 |  | 81 |  | 0204
2.565 |  | 80 |  | 0201
2.560 |  | 80 |  | 0200
2.555 |  | 80 |  | 01FF
2.540 |  | 7F |  | 01FC
0.020 |  | 01 |  | 0004
0.005 |  | 00 |  | 0001
0.000 |  | 00 |  | 0000
not
allowed
not
allowed

## Slide 28: ATD Status Register 0 (ATD0STAT0)
SCF: Sequence complete flag
ETORF: External trigger overrun flag* (indicates trigger occurred while previous conversion still in progress)
FIFOR: FIFO overrun flag* (indicates result register has been written before corresponding conversion complete flag (CCF) has been cleared)
CC2, CC1, CC0: Conversion Counter*
Points to the result register that will receive the result of current conversion
ATD Result Registers ATD0DR0 ~ ATD0DR7
  eight 16-bit result registers
SCF
0
ETORF
FIFOR
0
CC2
CC1
CC0
7
6
5
4
3
2
1
0
0
0
0
0
0
0
0
0
Reset:

## Slide 29: ATD Input Enable Register (ATD0DIEN)
IENx: When IENx=1, pin ANx can be used as a general purpose parallel port digital input pin rather than an A/D analog input pin
In this case, digital inputs are read from corresponding bit positions of PTAD0
IEN7
IEN6
IEN5
IEN4
IEN3
IEN2
IEN1
IEN0
7
6
5
4
3
2
1
0
0
0
0
0
0
0
0
0
Reset:
ATD Conversion Timings:

## Slide 30: Multichannel Example
Assume the following setup:
  Channel select code (CC ~ CA) of ATD0CTL5 = 6
  Conversion sequence length (S8C ~ S1C) of ATD0CTL3 = 5
  MULT bit of ATD0CTL5 is set to ‘1’ (i.e. multiple channels)
How would conversion results be stored in data registers?
Analog Channel | Result stored in: (non-FIFO mode)
AN6 | ATD0DR0
AN7 | ATD0DR1
AN0 | ATD0DR2
AN1 | ATD0DR3
AN2 | ATD0DR4

## Slide 31: Procedure for Performing A/D Conversion
Set up A/D power supply & reference voltages:
  VDDA: connect to 5V (nominal – normally same value as VDD)
  VSSA: connect to 0V (nominal – normally same value as VSS)
  VRH: connect to 5V (nominal) VRH ≤ VDDA
  VRL: connect to 0V (nominal) VRHL ≥ VSSA)
If transducer output is not in range (VRL ~ VRH), use a signal conditioning circuit to shift and scale it to match this range
Configure ATD control register 2 and wait 20ms for ATD circuits to stabilize
Configure ATD control registers 3 and 4.
Select appropriate channel(s) and operation modes by programming ATD control register 5. Writing to ATD0CTL5 starts conversion sequence
Wait until SCF flag of ATD0STAT0 is set, then collect conversion results and store in memory

## Slide 32: Example: A/D Initialization
Write a subroutine to initialize the AD0 converter with the following settings:
  Software initiated conversions (no external trigger)
  Fast ATD flag clear all
  No interrupts
  No FIFO mode
  10-bit operation
  2 MHz conversion clock (assume E-clock = 8 MHz)
  2 conversion clock periods for second stage sample time
  Sequence of n (1 ≤ n ≤ 8) conversions where n is passed in acc A
Need to write following data into ATD registers:
  ATD0CTL2: $C0
  ATD0CTL3: $00 + (n<<3)
  ATD0CTL4: $01
We do not write to ATD0CTL5 at this stage because that would actually start a conversion

## Slide 33: A/D Initialization Code
include “hcs12.inc”
openAD0: movb $C0, ATD0CTL2
jsr wait20us ; wait for A/D circuits to stabilize
ldab #8
mult ; left shift sequence # by 3 places
stab ATD0CTL3
movb #$01, ATD0CTL4
rts
wait20us: movb #$90, TSCR2 ; enable TCNT & fast timer clear
movb #0, TSCR1 ; set TCNT pre-scaler to 1
bset TIOS, $01 ; enable OC0
ldd TCNT ; start OC0 operation
addd #160 ; 160 clock cycles = 20 us
std TC0
brclr TFLG1, $01, * ; wait for time-out
rts

## Slide 34: Example: Perform 20 A/D Conversions
Write a program to perform A/D conversions on the analog signal connected to pin AN6. Collect 20 10-bit conversion results and store them in consecutive 16-bit memory locations starting at $1000. Data should be unsigned and right justified.
Solution: Initialize A/D to perform sequence of four conversions and then initiate five conversion sequences
HCS12
AN6

## Slide 35: 20 Conversions Code
include “hcs12.inc”
ORG $4000
lds #$4800
ldx #$1000 ; use X as data pointer
ldaa #4 ; sequence length = 4
jsr openAD0 ; initialize A/D converter
ldy #5 ; loop counter
loop5: movb #$86, ATD0CTL5 ; start ch6 A/D conv. sequence
brclr ATD0STAT0, $80, * ; wait for sequence complete flag
movw ATD0DR0, 2, x+ ; collect and save results
movw ATD0DR1, 2, x+ ; incrementing pointer by 2
movw ATD0DR2, 2, x+
movw ATD0DR3, 2, x+
dbne y, loop5 ; are we done?
swi

## Slide 36: Example: Record Potentiometer Output Voltage
Write a program to read the voltage from a potentiometer connected between 0 and +5 volts. The wiper of the potentiometer should be connected to the AN3 pin of AD0. Read the voltage once every 2 seconds and print out (to 2 sig. figs.) on a terminal using the SPI0 RS-232 serial output
Solution: The conversion result 1023 will correspond to +5V. To convert A/D output to volts, divide by 204.6.
  Since we don’t have floating point, this can be done by multiplying by 10 and then dividing by 2046
HCS12
AN3
+5V
SCI0
RS-232

## Slide 37: Potentiometer Output Code
include “hcs12.inc”
CR: equ $0D ; ascii carriage return
LF: equ $0A ; ascii line feed
ORG $5000
headbuf: dc.b “Voltage = ”, 0
numbuf: dc.b “0.0 V”, CR, LF, 0 ; calculated digits stored here
ORG $4000
lds #$4800
ldaa #1 ; sequence length = 1
jsr openAD0 ; initialize A/D converter
forever: movb #$83, ATD0CTL5 ; start ch3 A/D conv. sequence
brclr ATD0STAT0, $80, * ; wait for sequence complete flag
ldd ATD0DR0 ; get 10 bit data
ldy #10 ; multiply data by 10
emul ; L.S. result in D
ldx #2046 ; divide by 2046
idiv ; quotient in X, rem in D

## Slide 38: Potentiometer Output Code (cont.)
exg x, d ; swap X and D
addd #$30 ; convert MSD to ascii
stab numbuf ; store in string buffer
tfr x, d ; remainder back in D
ldy #10 ; multiply remainder by 10
emul
ldx #2046 ; and divide by 2046
idiv ; quotient in X
tfr x, d ; fractional digit in D
addd #$30 ; convert LSD to ascii
stab numbuf+2 ; store in string buffer
ldx #headbuf
jsr putsSCI0 ; output header string
ldx #numbuf
jsr putsSCI0 ; output number string
ldy #20
jsr delayby100ms ; wait for 2 seconds
bra forever

## Slide 39: Example: Temperature Sensor TC1047A
Three pin temperature sensor whose output voltage is directly proportional to ambient temperature
Measures temp. in range of -40º C to +125º C
Describe circuit connection and write program to read temperature five times per second and output temperature (signed and rounded to nearest degree C) to external peripheral connected to port T.

## Slide 40: Temperature Sensor: Signal Conditioning
Output of temperature sensor is 0.1V ~ 1.75V
To effectively use input range of A/D (0 ~ 5V), need to:
  multiply by (5/1.74 = 2.874) which gives a range of 0.29 ~ 5.29V
  offset by (–0.29V) which gives a range of 0 ~ 5V
+
–
741
+ 12V
– 12V
-5V
+
–
741
+ 12V
– 12V
10kW
TC1047A
VOUT
+ 5V
HCS12
AN7
10kW
9kW
3.1kW
150kW
PT0~7

## Slide 41: Temperature Sensor: Digital Data Scaling
Following signal conditioning, range of analog input is 0 ~ 5V
Range of digital result is 0 – 1023
Represents temperature range of 165 ºC
Need to divide by 1023/165 = 6.2
  i.e. multiply by 10 and divide by 62
  this gives a range of 0 ~ 165
Finally subtract 40 to give a range of – 40 to + 125

## Slide 42: Temperature Sensor Code
include “hcs12.inc”
ORG $4000
lds #$4800
movb $FF, DDRT ; set up Port T as 8-bit output
ldaa #1 ; sequence length = 1
jsr openAD0 ; initialize A/D converter

## Slide 43: Temperature Sensor Code (cont.)
forever: movb #$87, ATD0CTL5 ; start ch7 A/D conv. sequence
brclr ATD0STAT0, $80, * ; wait for sequence complete flag
ldd ATD0DR0 ; get 10 bit data
ldy #10 ; multiply data by 10
emul ; L.S. result in D
addd #31 ; to round divisor
ldx #62 ; divide by 62
idiv ; quotient in X, rem in D
tfr x, d ; rounded quotient in D
subd #40 ; to give signed result
stab PTT
ldy #2 ; wait for 200 ms
jsr delayby100ms
bra forever